## Slide 1: Experiment Setting

## Slide 2: Forecast Horizon & Inputs
Objective: Predict next 48 half-hour slots (1 day) of electricity demand.
Input window (past 48 slots):
  Demand (MW) history
  Temperature history
  Calendar/time features (hour, day-of-week, weekend, holiday)
  Rolling statistics (e.g., daily avg, 7-day avg)
Output horizon (next 48 slots):
  Vector of 48 demand predictions

## Slide 3: How do we handle temperature?
[Past 48 slots]
-> [Model]
-> [Next day Demand forecast]
History-only input (baseline):
  Use yesterday’s temperature + demand.
  Captures daily cycles and “similar day” patterns.
  Limitation: cannot adapt if tomorrow is unusually hot/cold. (only in reality)
[Past 48 slots] + [Temp forecast 48 slots]
→ [Model]
→ [Next day demand forecast]
History + forecast input (realistic):
  Add forecasted temperature for next 48 slots.
  Allows demand forecast to adjust to heatwaves/cold spells.
  Depends on forecast quality, not true observed temps (no leakage).
Key decision:
Research upper bound: train/evaluate with observed future temps.
Deployment realism: train with forecast temps.

## Slide 4: Model with history-only data
With history-only inputs we can still:
  Train with hot-aware sample weighting (no leakage in inputs).
  Evaluate by slicing metrics on actual hot/cold/normal days.
  Compare feature sets on these slices to see which helps hot-day performance.
Given the 1-week deadline for modelling, we’d better stick to history-only inputs keeps the pipeline clean and avoids the complexity of sourcing or simulating future forecasts.

## Slide 5: Ex 1. Feature set comparison (history-only):
Baseline minimal (fs2_min: demand + temp).
Add time encodings (fs3_time).
Add calendar (fs4_cal).
Strong set (lags, rolling windows, calendar).
Hot-aware variant (sample weighting).
To answer a research question: “Which features make the model more robust, especially on hot days?”

## Slide 6: Ex 2. Hot-aware weighting experiments
Re-train with weights >1 for hot days (e.g., 2.0×).
Compare overall MAE/RMSE vs hot-day MAE/RMSE.
Report whether the trade-off (slightly worse normal-day accuracy, better hot-day accuracy) is worth it.

## Slide 7: Ex 3. Evaluation slices (history-only)
Slice performance by hot vs cold vs normal days.
Slice by hour-of-day (to see if hot-day ramps in the afternoon are hardest).
Plot MAE by horizon for hot vs normal/cold.
To demonstrate the model isn’t just accurate “on average” but has strengths/weaknesses in critical conditions.

## Slide 8: Ex 4. Baselines for context
Compare against persistence baseline.
To show that our models (inc. LSTM) + feature engineering can outperform simple rules.

## Slide 9
Scope Decision
“We restrict inputs to past history only (demand + temperature + calendar).”
“We focus our analysis on how feature sets and hot-aware training affect accuracy on extreme hot days.”
Evaluation Strategy
Report metrics overall + by day type (hot, cold, normal).
Explicitly test hot-aware weighting.
Compare against persistence baseline.

## Slide 10: Feature Engineered Data

## Slide 11: Core variables
y (demand): the target to forecast, in megawatts (MW).
temp: observed temperature at half-hour resolution, because electricity use (air-con, heating) responds strongly to heat and cold.
y_forecast: operator’s published demand forecast, which can act as a baseline.

## Slide 12: Calendar and time features
hour: numeric hour (e.g., 13.5 = 1:30pm).
dow (day of week): Monday = 0 … Sunday = 6.
is_weekend: 1 if Saturday/Sunday, else 0.
is_holiday: public holidays (from official NSW calendar).
is_long_weekend: captures when weekends connect to a holiday (Fri–Mon).
sin/cos encodings for hour of day and day of week: give the model a smooth sense of daily and weekly cycles.
Why?
  Demand patterns differ on weekdays vs weekends, and holidays shift behaviour.
  Cyclical encodings make it easier for the model to “see” that 23:30 and 00:00 are close in time.

## Slide 13: Temperature-based flags
is_hot_slot / is_cold_slot: flags if temperature at that half-hour >=30°C or <=5°C.
is_hot_day / is_cold_day / is_normal_day: flags entire days based on daily max/min temp.
Note:
  These don’t go into the model inputs (to avoid leakage), but are essential for evaluation and weighting.
  They let us measure accuracy separately on hot vs normal days and optionally train with more weight on hot days.

## Slide 14: Demand lag & rolling features
y_lag1: demand 30 minutes ago → captures immediate momentum.
y_lag48: demand at the same time yesterday → daily cycle.
y_lag336: demand at the same time last week → weekly cycle.
y_roll_mean_48: average demand over the last day → smooth baseline.
y_roll_std_48: variability of demand over the last day → indicates volatility.
y_roll_mean_336: average over the past week → weekly baseline level.

## Slide 15: Temperature lag & rolling features
temp_lag1 / lag2 / lag3: temp 30, 60, 90 minutes ago → short-term persistence (heat build-up).
temp_lag48: temp at the same time yesterday → daily thermal cycle.
temp_roll_max_48 / temp_roll_min_48: hottest and coolest temp in the last 24h → distinguish heatwaves vs single hot hours.
Demand reacts not just to current temperature, but to sustained heat/cold.
These features give the model context on how “extreme” current conditions are compared with the recent past.

## Slide 16: Why these features help for hot-day forecasting
Calendar features prevent misinterpreting holiday/weekend demand drops as weather effects.
Lag features help align the model with recurring daily and weekly shapes.
Rolling features provide baselines to measure unusual deviations (e.g., spikes on a hot day).
Temperature lags/rolls capture the persistence of heatwaves, critical for predicting cooling load.
Hot/cold flags allow us to evaluate or up-weight extreme days without leaking future information.